## Slide 1: ACCESS CONTROL LIST
-BA0

## Slide 2: What is an acl?
ACLs are an integrated feature of the CISCO IOS software that is used to filter traffic as it passes through the router or switch.
Unix like and Mac OS X operating systems contain filesystem ACLs that specify individual user or group rights to specific system objects such as program, processes and files.

## Slide 3: Networking acl
list of sequential permit and deny statements.
filter packets based on the above statements.
Can be inbound or outbound.
Powerful tool to control network traffic.

## Slide 4: What type of threats can it mitigate?
IP address spoofing, inbound
IP address spoofing, outbound
Denial of service (DoS) TCP SYN attacks, blocking external attacks
DoS TCP SYN attacks, using TCP Intercept
DoS smurf attacks
Denying/Filtering ICMP messages, inbound
Denying/Filtering ICMP messages, outbound
Denying/Filtering traceroute

## Slide 5
TYPES OF ACLs
Standard ACLs.(Source IP only).
Extended ACLs.(Evaluate Layer 3 and 4 information)
Named ACLs.(If you figure it out let me know)

## Slide 6
STANDARD ACL.
Use only source IP in the packet to test conditions.
Do not distinguish between protocols.
Every ACL has a number.
But that does not mean any number!
List of ranges:
<1-99> IP standard access list
<100-199> IP extended access list
<1100-1199> Extended 48-bit MAC address access list
<1300-1999> IP standard access list (expanded range)
<200-299> Protocol type-code access list
<2000-2699> IP extended access list (expanded range)
<700-799> 48-bit MAC address access list
compiled Enable IP access-list compilation
dynamic-extended Extend the dynamic ACL absolute timer
rate-limit Simple rate-limit specific access list

## Slide 7
Packet(IP header)
Standard ACL statements
Protocol
IP address
Permit
Deny

## Slide 8
How do you create one??
Router(config)#access-list <number> <permit/deny> <host> <IP address/any> <wildcard mask>
E.g. Router(config)#access-list 10 permit host 172.168.10.1

## Slide 9
Router
Internet
Student
Admin
192.168.10.16 /28
192.168.10.48 /28
Int G1/0
Int G1/2
Int G1/3

## Slide 10
EXTENTED ACLs.
Standard ACLs are not efficient since they can only check the source IP hence E-ACLs.
E-ACLs provide more granularity.
One can specify source IP address, destination IP address, protocol and port number.

## Slide 11
Syntax:
Router(config)#access-list <number> <permit/deny> <Protocol> <source> <destination> <eq/other options> <port number/ service name>
Other options are
Ack= Match on the ACK bit
Dscp= Match packets with given dscp value
Eq= Match only packets on a given port number
Established= Match established connections
Fin= Match on the FIN bit
Fragments= Check non-initial fragments
Gt= Match only packets with a greater port number
log =Log matches against this entry
log-input= Log matches against this entry, including input interface
Lt= Match only packets with a lower port number
Neq= Match only packets not on a given port number
Precedence= Match packets with given precedence value
Psh= Match on the PSH bit
Range= Match only packets in the range of port numbers
Rst= Match on the RST bit
syn =Match on the SYN bit
time-range= Specify a time-range
Tos= Match packets with given TOS value
urg =Match on the URG bit

## Slide 12
Data
Segment(T layer header)
Packet
Extended ACL(Numbers 100-199 0r 2000-2699) statements.
Port Numbers
IP add
Deny
Protocol
Permit

## Slide 13
Router
web
DNS
Switch
Switch
Int 0/1
Int 0/0
Int 0/2
192.168.10.2
192.168.10.3
172.16.15.3
172.16.15.2

## Slide 14
Router(config)#access-list 110 permit tcp host 192.168.10.2 host 172.16.15.3 eq 21
Router(config)#access-list 110 deny tcp any host 172.16.15.2 eq 80
Router(config)#access-list 110 permit tcp host 192.168.10.3 host 172.16.15.2 eq 23
Router(config)#access-list 110 deny tcp any host 172.16.15.2 eq 23

## Slide 15
Most Important!!!!!!
Standard access lists placed close to the destination since it has to check source IP while extended placed close to the source since it can check port destination etc.
There is always an implicit deny at the end of an access list!
Do not forget to add the permit any command. Router(config)#access-list 110 permit any any